## Slide 1: Procedure 02 – ROBOTC Inputs/Outputs
Basic Output Programming
Basic Input Programming
Lafayette Jefferson High School – Intro to Communications – Mr. White

## Slide 2: ROBOTC Output Programming
Ensure Procedure 01 has been followed and all connections are set.
Here is an example of a program for a flashlight that would be typed in the task main() section of the program between the curly braces.
Lafayette Jefferson High School – Intro to Communications – Mr. White
turnLEDOff(green); wait(1); turnLEDOn(green); wait(1); turnLEDOff(green); wait(1); turnLEDOn(green); wait(1); turnLEDOff(green);

## Slide 3: ROBOTC Output Programming Cont’d.
Write a program that performs the following simple behaviors. Use the natural language functions where appropriate as shown below. Add comments at the end of each command line to explain the purpose of each step.
  Turn the rightMotor on forward at half speed for 5 seconds.
  Stop the motor.
Lafayette Jefferson High School – Intro to Communications – Mr. White
Natural Language – Movement
Natural Language – Wait
Natural Language – Until

## Slide 4: ROBOTC Output Programming Cont’d.
Test the program and troubleshoot if needed until the expected behavior has occurred.
Modify the program above to include this simple behavior.
Turn on leftMotor at the same time that rightMotor is turned on.
Test the program and troubleshoot if needed until the expected behavior has occurred.
Modify the program above to include this simple behavior.
Reverse both motors using two different programming methods.
Test the program and troubleshoot if needed until the expected behavior has occurred. Save the program.
Lafayette Jefferson High School – Intro to Communications – Mr. White

## Slide 5: ROBOTC Output Programming Cont’d.
Write a program that performs the following simple behaviors. Use the natural language functions where appropriate as shown below. Add comments at the end of each command line to explain the purpose of each step.
  Turn the rightMotor on forward at half speed for 5 seconds, then stop.
  Turn the leftMotor on in reverse at three-fourths speed for 2.5 seconds, then stop.
  Turn both motors on at full power, and spinning in the same direction, for 7.25 seconds, then stop.
Test the program and troubleshoot if needed until the expected behavior has occurred.
Power on the Cortex and Compile and Download the program. If you have any errors, check with your instructor to troubleshoot your program.
Lafayette Jefferson High School – Intro to Communications – Mr. White